TURBO ROM

		    Theory of Operation


The TURBO ROM for Kaypro computers interfaces the CP/M operating
system to the actual hardware such as video display and disk drives.
It allows the addition of expansion hardware such as high capacity floppy
disks, multiple hard disks and Advent Products RAM disks.  It automatically
senses the presence of this hardware and provides the appropriate drivers
to allow the operating system to fully use these new devices.


The following notes may be useful to those wishing to understand the
operation of the ROM.


COLD BOOT
When power is applied, or the reset button is pressed, the following sequence
of events is followed.  
	1/ A delay of 100 ms to allow for some of the peripheral chips to
	achieve equilibrium.  (MOSTEK parts are much slower than Zilog)

	2/ The peripheral devices are programmed with default values such
	as baud rate etc.

	3/ The video driver is initialized and the screen cleared.

	4/ The sign-on message is printed.

        5/ The presence of the WD1002 hard disk controller is detected, by
        seeing if it comes not busy within 3 seconds.  If so, drive one is   
        tested for ready.  We wait up to 20 seconds for it to come up to
        speed.  (Note Drive One is connected to J2 of controller)

	When ready we issue a restore command and wait up to 25 seconds for
	the completion.  (If any of these tests fail then we have no hard
	disk)

	7/ An attempt is then made to read a 1024 byte sector (8) from the
	first cylinder of the disk.  If this is successful then we check to
	see if the sector is a valid parameter sector.  On 83 machines the
	main part of the hard disk initialization code is contained on the
        second half of the sector.  The first 512 bytes of this parameter
        sector contain the characteristics of the drives and the bad track
        mappings.

	*84 Machines Only
        If this read fails we attempt to read a 512 byte sector (16) from
        the same cylinder. If this is successful we check for valid
        parameter sector.

	If we have a succesful 512 byte sector read but an invalid sector then
        we assume 512 byte sectors of standard Kaypro layout.

	8/ *83 Machines Only
        The code read from the parameter sector is used to check for the
	presence  of a second Hard disk.  Parameter tabels for these drives
	are set up in memory along with bad track maps.

	9/ The lowest (in terms of select logic 0,1,2,3) floppy drive is
	examined for the presence of a spinning diskette.  If detected the
	logical drive ordering is as follows:
		A -> V  = Floppy Drives
		X -> Y	= Hard Drives		(if present)
		Z	= Ram Disk		(if present)

	If no floppy detected the logical drive ordering is:
		A -> V	= Hard Drives		(if present)
		X -> Y	= Floppy Drives
		Z	= Ram Disk		(if present)


	10/ An attempt is then made to read the first sector of
	logical drive "A".  This parameter sector conforms with the
	standard Kaypro layout, having the load address, execution address
	and the number of sectors to be loaded.  If we are running on a
	Kaypro  10 with a 512 byte/sector hard disk a check is done to see
	if the system to be loaded will over-write the Host Buffer area
	(see memory layout for explanation), and if this occurs (generally
	only with a 63K system) the Host buffer is shortened to 512 bytes and
	floppy disk formats with > 512 bytes/sector are flagged as illegal.

	11/ The system is then read into memory and control is tranferred
	to this system at the specified address.  If the supplied
	TURBO-BIOS is used (highly recommended) then further initialization is
	performed.  The nature of this initialization can be modified by
	the supplied configuration program TURBOCFG.


WARM BOOT
On a Warm Boot an attempt is made to read from the logical "A" drive a
fresh copy of the Command Processor and Basic Disk Operating System (BDOS).
The configuration program TURBOCFG can be used to change the default drive
for this operation.  We recommend using this advanced option only if you
really know what you are doing.  An example may be to warm boot from the
RAM disk without making it drive A. However, it must be SYSGENed before the
first warm boot takes place.

DISK SELECT (and Deselect)
Floppy drives have removable media while Hard Disks and Ram Disks have fixed
media.  Drives with removable media are treated differently at select time.
If this is the first select since a disk reset then we re-determine the
format of the diskette in the drive.  (This operation can be inhibited
under special circumstances).  If the format cannot be determined a BDOS
Select error will occur, unlike most BIOS's which would generate a bad
sector error.  Naturally a select error will also occur if an attempt is
made to access a non-existent drive.

A period of time after the last disk operation, a deselect process occurs.
This first makes sure the contents of the De-Blocking buffer are written
back to the disk if required.  Then the floppy motor is turned off and if
needed both floppy drives are deselected (lights turned off).  If Hard
disks are present then each drive seeks the innermost formatted cylinder
and then non-existent drive zero is selected.  This final step deselects
the actual hard drives.




		   DEFINITION OF TABLES USED BY THE ROM


DATA PARAMETER HEADERS (Commonly alled DPH's)

The DPH for each logical drive is extended by 2 bytes compared to the
standard DRI definition (see CP/M manual if you are not familiar with
this).  These 2 bytes preceed the normal 16 bytes.

The first byte contains information on the logical/physical mapping of the
drives. 
------------------------------------------------------------
Byte0	-	logical/physical drive mapping

physical:
	bit 7		-- reserved for future use by Plu*Perfect Systems
	bit 6,5,4
			000  = Advent Products RAM disk (up to 2 MBytes)
			001  = reserved for future use
			010  = Physical Hard Drive 0	(up to 56 MBytes)
			011  = Physical Hard Drive 1	( "   "   "     )

			100  = Physical floppy 1	(48 or 96 TPI)
			101  = Physical floppy 2
			110  = Physical floppy 3
			111  = Physical floppy 4



logical:
	bit 3-0		logical drive A-P
			0000	=	A
			0001	=	B
			0010	=	C
			  .             .
			  .		.
			  .		.
			1111	=	P

______________________________________
In the second byte, some physical charactistics of the Drive are
coded.

Byte1	-	drive characteristics byte defined as follows:-
****************FLOPPY DRIVE

	bit 7	-	0  = if drive is 48 tpi
			1  =   "   "     96 tpi


	bit 6	-	0  = redetermine media on fresh select(normal)
			1  = don't redetermine media on fresh select
				(used when externally set disk format)


	bit 5	-	unused

*****************HARD DRIVE
	Advent Format -
	bit 7,6,5	number of heads (minus one)


	Kaypro 512 byte/sector format-
	bit 7		0 = platter A (heads 0,1)
			1 = platter B (heads 2,3)

	bit 6,5		unused

*****************RAM DRIVE

	bit 7,6,5	unused

***********
All drive types

	bit 4	0  = Use ROM DPB tables
		1  = Use RAM DPB tables

	bits 3,2,1,0	Use DPB 0-15 from rom or ram table


Bytes
2 - 18	-	Standard DRI data parameter header. 



DATA PARAMETER BLOCK (DPB's)


The DPB's used by the ROM are 3 bytes longer than the standard definition
given by DRI (see CP/M manual if you are not familiar with this).  These 3
extra bytes precede the normal 15 bytes.

There is a word which points to a sector translation table address.  This
may be zero,  a ROM address which is not accessable to external programs
without bank switching, or an externally loaded table in high RAM.

There is then a Byte which characterizes the type of format associated with
this DPB. The bits in this byte are interpreted as follows:


1/ For Floppy Drives: (Media)

	bit 7	-	0  = disk is in 48 tpi format
			1  = disk is in 96 tpi format

	bit 6	-	0  = standard data sense
			1  = inverted data bus (only available on 84 ROM)
				(used only on machines that used chips
				like 1771/91 without inverters)

	bit 5	-	1  = single density
			0  = double density

	bit 4,3,2   -	Use algorithm 0-7 to compute physical
			cylinder, track, sector and side. 
			Note algorithm 7 is reserved for external
			code, which the user may load.  See later for
			definition and how to load this code.

		Predefined Algorithms
		-----------------------------------------------
		000	- for 512 byte Kaypro hard disk format
						(see below)
		-----------------------------------------------
		001	- for 512/1024 byte Advent hard disk formats
						(see below)
		-----------------------------------------------
		010	- single sided floppy
			phy.cylinder	=track
			phy.track	=track
			phy.sector	=sector
			phy.head(side)	=0
		-----------------------------------------------
		011	- double sided Kaypro/Advent floppy
			bias		=10
			phy.cylinder	=int(track/2)
			phy.track	=phy.cylinder
			phy.head(side)	=mod(track,2)
			phy.sector	=sector + side*bias
		-----------------------------------------------
		100	- Micro Cornucopia/Advent 96 tpi,
			Same as Kaypro except
			bias		=20
		-----------------------------------------------
		101	- double sided (single long track)
			Note that zero based sector numbering assumed,
			fits Legacy formats

			phy.cylinder	=track
			phy.track	=track
			phy.sector	=sector
			phy.head(side)	=0 if sector < phy_sect/side
					=1 if sector >=  phy_sect/side
		-----------------------------------------------
		110	- double sided (odd tracks on back but no sector skew)
			Same as Kaypro except
			bias		=0
		-----------------------------------------------
		111	- External routine, parameters
			  in registers on call and return.

			ENTRY				EXIT
	HL	none				physical cylinder to seek
	DE	HSTTRK				physical track for floppy ctrl
	B	HSTDRV (dph byte 1)		physical head (side)
	C	HSTSEC				physical sector

		------------------------------------------------

	bit 1,0	-	00 = 128 physical sector length
			01 = 256
			10 = 512
			11 = 1024

-------------------------------------
2/ For Hard Disk Drives:



	bit 7,6,5		unused


			(These bytes compatible with floppy use)
	bit 4,3,2	000	-Kaypro 10 original format
			   512 byte  sectors (algorithm for track sector)
				phy.cylinder	= (track + offset)/2
				offset = 0		if track < 4
				offset = track - 4 	if 3 < track < 8
				offset = 4		if track > 7

				phy.track	= n/a
				phy.sector	= sector
				phy.head	= mod(track+offset,2)
							 + drvbyt(7)*2
				drvbyt(7) is bit 7 of byte 1 of DPH

			(note we abandon trying to maintain
			duplicate directory on back of platter,
			if problems, then reformat with our new
			format)

			001	-Advent Hard disk format
			    512/1024 byte sectors
				phy.cylinder	= trackx/#heads
				phy.track	= n/a
				phy.sector	= sector
				phy.head	= mod(trackx,#heads)

			(Note trackx = badfnc(track).  This corrects
			desired track for bad tracks.  The bad track
			function is performed by the following algorithm.

			I:=0
			TRACKX:=TRACK
			DO WHILE(BADTRK(I) >= TRACK)
				TRACKX:=TRACKX +1
				I:=I + 1
			END


			Where badtrk(i) is a list of bad physical
			tracks which is terminated with FFFFH entry.
			We support a maximum of 126 bad tracks per physical
			drive.)

	bit 1,0	-	00 = not supported
			01 = not supported
			10 = 512 byte sectors (only available on 84 ROMs)
			11 = 1024 byte sectors

------------------------------------------------
3/ Advent Ram Disk Drive:

	bit 7,6,5,4,3,2	unused


	bit 1,0	-	00 = 128 byte sectors
			01 = not supported
			10 =	"    "
			11 =    "    "

-------------------------------------------------

In ROM we have a maximum of 16 DPB's
DPB#

0	Standard Kaypro SS (512 byte sectors)				floppy
1	Standard Kaypro DS (512 byte sectors)				floppy
2	Advent SSDD 448 tpi(1024 byte sectors) ( handles Osborne SSDD)	floppy
3	Advent DSDD 48tpi (1024 byte sectors)				floppy
4	Advent DSDD 96tpi (1024 byte sectors)				floppy
5	Micro C DSDD 96tpi (512 byte sectors)				floppy
6*	Xerox 820 SSSD	(128 byte sectors)				floppy
7*	Osborne SSSD (256 byte sectors)					floppy
8*	Epsom QX-10 (U.S. format - not European)			floppy
9*	Kaypro 10 (original hard disk format)				hard
10*
11*
12*
13*		reserved for future expanison
14*
15*

* only available on 84 ROMS


In high memory we store the DPB's who have to be dynamically changed/added.
The first DPB is a reserved entry for use by external programs who wish
to set up a foreign floppy format for the ROM to work with.

The second is always the RAM disk if it exists.  Following this are the
various Hard disks (Advent Format only) which are actually read in from the
parameter sector of the hard disk.  These DPB's are stored in descending
memory order (unlike DPH's above).




			  HIGH MEMORY ARRANGEMENT

The ROM uses the very top of the Kaypro RAM for its working storage.  The
amount of memory used depends on the physical configuration, but in all
cases, memory is dynamically allocated at cold boot time so that the amount
of memory available to user programs is maximized.  The very top of memory
is of fixed layout (which varies slightly between 83 and 84 ROMs) and this
is useable by programs which need to find out about the current environment.


topmem		equ	0FFFFH
;*************************
;ROMID is 8 byte string of following layout
;		db	checksum	;zero sum of top 8 bytes in memory
;		jmp	romentry	;general ROM entry point
;		db	version		; BCD ver.rev, (hi bit set '84)
;		db	'PPS'
;*************************
;fixed pointers and storage which are guarranteed to be preserved in
;future releases of the ROM

dphptr:	dw	numdrv		;pointer to start of DPH table
dpbptr:	dw	numdpb		;pointer to start of RAM DPB's
hstptr:	dw	hstbuf		;pointer to Host buffer
				;This is the lowest area used by ROM
intptr:	dw	intvec		;pointer to start of interrupt vector
extptr:	dw	tsalgr		;pointer to external trk/sctor code
hrdptr:	dw	badtr0		;pointer to hard/floppy disk parameters

;fixed storage that varies between 83 and 84 machines
	83					84
     --------				      ---------
safptr:	dw	safcod				dw	x	;reserved
cursor:	dw	x			cursor:	dw	x	;video cursor
					clkent:	dw	clkdrv	;routine to
								;clock
					curmin:	db	minutes	;current time
						db	hours
;***********************
	Interrupt vector for all devices.
	83				84
     --------			     --------
					pioBvc	;modem dialer
					pioAvc	;RTC interface

					sioCv3	;serial printer
					sioCv2
					sioCv1
					sioCv0

	pioDvc	;unused			sioDv3	;Modem or Unused serial
	pioCvc	;printer		sioDv2
	pioBvc	;unused			sioDv1
	pioAvc	;system port		sioDv0	;

	sioAv3				sioAv3	;serial data char rec.(error)
	sioAv2				sioAv2	;serial data char rec.
	sioAv1				sioAv1	;serial data ext. status
	sioAv0				sioAv0	;serial data Tx buffer

	sioBv3				sioBv3	;keyboard char rec. (error)
	sioBv2				sioBv2	;keyboard char rec.
	sioBv1				sioBv1	;keyboard ext. status
	sioBv0				sioBv0	;keyboard Tx buffer

intvec:						;start of vectors aligned on 
						;16 byte boundary

;*********************
	Stack space for interrupt handlers and ROM

;********************
	Code, DIRBUF and other variables
;********************
	Area for externally defined floppy drive
	information


xtran:	ds	36		;36 bytes of physical translation table

	ds	55		;SPACE for code referred by labels
				; invmap and mapit

	db	fmt				;current format number
	jmpr	invmap				;inverse trk/sector/side
tsalgr:	jmpr	mapit				;cylinder/sector/head
;********************
Miscellaneous disk/video/and other variables
which may change with future ROMS implementation.

		-----------
However the following structure will remain intact though
it will doubtless move.

disblk:	db	..	;84 machine video blanking disable (00/FF)
							(not currently used)

smflag:	db	..	;84 machine retricted to 512 byte sectors

stldly:	db	z	;current floppy head settling delay (ms)
hldly:	db	y	;current floppy head load delay(ms)
fstprt:	db	x	;current floppy step rate (ms)

ftime4:	db	x,y,z	;array of floppy time constants for each drive
ftime3:	db	x,y,z
ftime2:	db	x,y,z
ftime1:	db	x,y,z

muxflg:	db	..	;flag for presence of Advent decoder board
fstat:	db	..	;current floppy arrangement
			;7 - Drive 4 96 tpi
			;6 - Drive 4 exists
			;5 - Drive 3 96 tpi
			;4 - Drive 3 exists
			;3 - Drive 2 96 tpi
			;2 - Drive 2 exists
			;1 - Drive 1 96 tpi
			;0 - Drive 1 exists (always true)

wdflag:	db	..	;7 - if parameter sector successfully read
			;0 - WD 1002 controller detected

sltmsk:	db	..	;floppy select mask
			; 00000011B	;normal 2 lines
			; 00000001B	;Kaypro 10 hard disk connected

precp1:	db	..	;Hard Drive 2 precomp cylinder(coded)
step1:	db	..	; "     "   " step rate (coded)
mxcyl1:	dw	...	; "     "   " maximum formatted cylinder
badtr1:	dw	list1	; "     "   " pointer to start of bad track table

precp0:	db	..	;as above for drive 1
step0:	db	..
mxcyl0:	dw	...
badtr0:	dw	list0	;POINTED TO BY HRDPTR AT TOP OF MEMORY


polflg:	db	..	;set to 00 if type-ahead keyboard (else FF)
belchr:	db	..	;bell character for keyboard, may have click bit
			---------------

********************************

		**************************************
		*  Run time determined storage areas *
		**************************************



Actual list of n*18 drive descriptor bytes where n is logical number of
drives.  These are arranged as described above.

numdrv:		db	n		;logical number of drives
					;pointed to by dphptr


	Followed by DPH for each drive as described above.
	NOTE that DPH's ascend in memory above the NUMDRV byte.


************************************************************
In RAM DPB tables decribed above -- note they descend in memory
though the number of DPBs  byte is still at bottom of list

each DPB of following layout

	dw	xtran ptr
	db	media byte
	ds	15			;normal DRI definition

Actual list of RAM dpb's in following order (descending in memory)

0 -	always externally definable floppy
1 -	RAMDISK (computed at cold boot)

2-15	up to 14 more formats read in from hard disk
	parameter sector

	(future ROM releases may limit number of logical hard disks to 13)

numdpb:		db			;number of RAM dpbs in this
					;configuration, the first
					;is always the externally
					;definable floppy

;***********************
;Hard Disk bad track lists  (if any)

list1:	dw	...
	dw	...
	dw	FFFFH

list0:	dw	...
	dw	...
	dw	FFFFH
************************
hstbuf:	ds	1024			;deblocking buffer
					;init code changes to 512
					;bytes if system loaded too high
					;on Kaypro 10 with 512
					;byte sectors

************************

lowest area used in high Ram by ROM






		    ADVENT PRODUCTS ELECTRONIC RAM DISK

The RAM disk is located at ports 88H thru 8BH.


88H	-	data bi-directional
89H	-	sector (6 lo bits only)
8AH	-	track register (7 lo bits per board, hi bit board select)
8BH	-	status register	(bit 0,1  00,01,10,11 are 256,512,768,1024K
			respectively.  Bit 2 is 0 if board is present and
			otherwise is pulled up.


Status register returns
xxxxx000	= 256k
xxxxx001	= 512k
xxxxx010	= 768k
xxxxx011	=1024k
xxxxx1xx	= ram disk not present

Then we write 8AH with 80H and repeat read of 8BH for second board.


RAMDISK has following DPH

XLT ptr		0000		;no sector translation
SCRATCH		0000
		0000
		0000
		DIRBUF		;pointer to directory buffer
		CURDPB		;always points to DPB current
		0000		;no directory checksum
		ALVRAM		;pointer to size dependent area


RAMDISK has following DPB
XTRN:	dw	0000		;no sector translation
MEDIA:	dw	00		;128 byte sectors
SPT:	dw	64
BSH:	db	x		;x = 3 for 256K
				;  = 4 for 512K
				;  = 5 for 768,1024K
				;  = 6 for > 1024K

BLM:	db	2**x - 1
EXM:	db	2**(x-3) - 1
DSM:	dw	2**(6-x).(n+1).2**5 - 1) - 1
DRM:	dw	2**(3+x) - 1
AL0:	db	0C0H
AL1:	db	000H
CKS:	dw	0000
OFF:	dw	0001



Sector 63 of track 0 is initialized with a copy of the first
128 byte of the ROM.  On subsequent resets this is compared and
if a match is detected the directory of the RAM disk is not erased.
*************************************************




		       FLOPPY DISK FORMATS

The Turbo ROM will recognize and can use directly the following floppy disk
formats:- 

	83					84
     ---------				      ---------
Kaypro SSDD				Kaypro SSDD
Kaypro DSDD				Kaypro DSDD
Advent SSDD				Advent SSDD
Advent DSDD 48				Advent DSDD 48
Advent DSDD 96				Advent DSDD 96
Micro Cornucopia 96			Micro Cornucopia 96

					Epson QX-10 DSDD 48 (U.S.)
					Osborne SSSD
					Xerox 820-1 SSSD


In addition any other CP/M 5.25" soft sector format may be set up using the
TURBOSET program which is available separately as part of the Plu*Perfect
Systems' MULTI-COPY package.


The Advent formats mentioned above have the following description.

1) SSDD

	Physical Sector Length		1024 bytes
	Physical Sector Order		1,4,2,5,3

	Logical Sectors/Track		40
	Number of Cylinders		40
	
	Reserved Tracks			3
	CP/M allocation size		1K
	Directory Entries		64
	Reserved Directory Groups	2
	Total size			185K

	*note that this format is identical to the Osborne SSDD
	except for the physical sector order

2) DSDD 48

	Physical Sector Length		1024 bytes
	Physical Sector Order		1,4,2,5,3	-side 0
					11,14,12,15,13	-side 1

	Logical Sectors/Track		40
	Logical Tracks			80
	Number of Cylinders		40
	Reserved Tracks			2
	CP/M allocation size		2K
	Directory Entries		256
	Reserved Directory Groups	4
	Total size			390 K


3) DSDD 96

        Physical Sector Length		1024 bytes
	Physical Sector Order		1,4,2,5,3	-side 0
					21,24,22,25,23	-side 1

	Logical Sectors/Track		40
	Number of Cylinders		80
	Number of Logical Tracks	160

	Reserved Tracks			2
	CP/M allocation size		2K
	Directory Entries		256
	Reserved Directory Groups	4
	Total size			790 K




			 TURBO ROM VIDEO FEATURES


The Turbo ROM provides a number of new video features compared with the
standard Kaypro.  These differ between the 83 and 84 versions.

Video Blanking:

Both ROM's provide a screen saving video blanking after about ten minutes
of waiting for keyboard input.  However, on 83 machines this feature
requires a modification to the video circuit.  This is optional and the
blanking will not occur unless the change has been made.  Because the ROM
has no way of knowing whether the change has been made, the unblanking
keystroke will not be ignored as it is with the 84 ROM.

The 83 video change is made simply by purchasing a replacement character
generator ROM and putting it into the circuit.  Alternatively, people with
electronic circuit experience, can make a small modification to the main
circuit board to achieve the same effect.  Details are available on request.

Screen Dump:

While not a direct feature of the Turbo ROM, the TURBO BIOS supplied with
the ROM has character (not graphic) screen dump to printer capability.  The
ROM actually provides the support for this feature but it must be
externally activated, for more details see the source code to the BIOS and
the following description of the ROM Entry Points.  The Screen Dump must be
explicitly enabled by using TURBOCFG.


Changes to Video Control Codes and Escape Sequences:

Some changes to the behaviour of the video compared to the standard Kaypro
ROM's have been made.  These are generally for consistency or to correct
bugs in the original implementation.

a) Control Characters that are not used by the video are now "swallowed"
rather than generating Greek characters or Fine Line graphics.

b) On 83 machines the underline cursor no longer destroys true underline
characters on the screen when moved through their positions.

c) On 84 machines the ESC G/ESC A sequences are implemented identically to
the 83 machines.  That is the 32 characters (lower case) from the grave
accent (60 Hex) through the DELete (7F Hex) will produce the the
corresponding graphic character in position 0-31 (decimal) in the character
ROM if the video sequence ESC G has been recieved.  When the sequence ESC A
is recieved the lower case characters produce themselves.  On the 83
character ROM's thes 32 characters are normally greek and mathematical
symbols.  On the 84 character ROM's these characters are normally the Fine
Line graphic set.  On Foreign Language Kaypro's these characters are
selected european characters.

d) On 84 machines the sequences ESC B 7/ESC C 7 have a slightly different
effect.  The standard video defaulted to a 24 line scrolling window with
the 25th line also scrolling.  The Turbo ROM is either a 25 line scrolling
display or a 24 line scrolling display with the 25th line locked.  The
difference is minor unless you wish to reconfigure some of your application
programs to make use of the 25 line screen.  Note that the ROM scrolling is
much faster if a 25 line scrolling region is enabled.  Also, scrolling is
much faster if no video attributes have been used since the last clear screen.

New Features:

a) Hard Tabulations.  The standard video ignored the tabulation character,
"^I".  Both 83 and 84 ROM's expand this to 8 column fixed tabs.  This is
mostly of use to user's of Plu*Perfect Systems NOTEPAD module of the
Backgrounder, as most programs expand tabs in software.

b) Insert and Delete Character.  Two new control codes are now interpreted
to insert and delete characters. "^A" will cause the next character
recieved to be inserted at the current cursor position.  "^B" will delete the
character currently at the cursor position.  Both of these controls are
limited to the current line, i.e. inserting characters will move the
characters to the right of the cursor but will not cause any that are
displaced past the end of the line to wrap.  These new features are again
of interest to users of Plu*Perfect Systems' NOTEPAD module of the
Backgrounder.

c) On 84 machines there is now a method of dynamically modifying the type
of cursor used.  ESC U n will cause a new cursor whose characteristics are
defined by the ascii character "n".  The cursor is bit encoded into this
character and the bit positions have the following meaning.

	bits 6,5		- blinking
			00 - no blinking
			01 - no cursor
			10 - fast blinking
			11 - slow blinking
   
	bits 4,3,2,1,0		- cursor height

			00000 - full block cursor (16 scan lines)
			00001 -
			00010 -

			.....

			01110 - thicker underline     (2 scan lines)
			01111 - thin underline cursor (1 scan line)

d) Disable on screen clock display.  On 84 machines which have either a
built in Kaypro clock or and Advent Products clock, the on screen display
of the time may be temporarily disabled with

	ESC C 8  and re-enabled with ESC B 8

Note that the clock display is automatically disabled if a 25 line
scrolling screen is selected.

e) Switch character generators. On 84 machines which are correctly wired,
an altenate character set may be chosen with the following

	ESC B 9 and the original re-selected with ESC C 9

This additional character set would normally reside in the other half of a
27644 character ROM.  True 84 machines are actually wired to accept this
chip but unfortunately Kaypro did not test the circuit and a minor
modification is required.  On older Kaypro 10's a small circuit
modification is required, please contact Advent Products if you wish to
make use of this feature of the TURBO ROM.






		      ENTRY POINTS INTO THE TURBOROM

The TURBO ROM in general preserves the standard entry points that have been
used with only small differences by all CP/M Kaypros since the KAYCOMP.
There are naturally some extensions which provide additional features.  One
major addition is the creation of a standard entry mechanism that can be
used regardles of whether an 83 or 84 machine is being used.

If a utility wishes to call the ROM it should load the page zero address it
wishes to call into the L register and then call 0FFFCH in high memory. 
All the bank and stack switching tasks will be automatically taken care of. 
However, direct calls to the ROM should be avoided in normal application
programs as they severely limit portability of the program.

Entry Points:
0000	Machine Restart,  cold boot
0003*	Disk Reset
0006	Initialized video driver
0009*	Initialize unit record hardware	
000C*	Deactivate Host buffer if not written (HOME)
000F	Select disk for next access
0012	Set Track for next disk access
0015	Set Sector for next disk access
0018	Set DMA address for next disk access
001B	Read Sector
001E	Write Sector
0021*	Sector Translation (dummy, delayed to SETSEC)
0024	Turn on the Floppy drive motor
0027*	Turn off floppy motors, Deselect hard drives, flush Host buffer
002A	Keyboard input status
002D	Keyboard input
0030	Keyboard serial output, use with caution
0033	Serial Data port input status (TTY)
0036	Serial Data port input (TTY)
0039	Serial Data port output (TTY)
003C	Centronics printer output status (LPT)
003F	Centronics printer output (LPT)
0042	Serial Data port output status (TTY)
0045	Video output (CRT)
0048*	Ten millesecond delay
004B#	Serial Printer input status (UL1)	[83=TTY]
004E#	Serial Printer input (UL1)		[83=TTY]
0051#	Serial Printer output (UL1)		[83=TTY]
0054#	Serial Printer output status (UL1)	[83=TTY]
0057#	Reload system
005A#	Get next screen dump character
005D#	Set cursor type
0060#	One millesecond delay
0063#	Initialize DPH -----DO NOT USE
		83 Roms					84 Roms
0067#	Hard Disk Seek -----DO NOT USE		0067#	Kaypro Clock
006A#	Hard Disk Setup-----DO NOT USE		006A#	Advent Clock
						006D#	Kenmore CLock





Rom Entry Point Specifications:
(* Changes from Original Kaypro)
(# New entry points)

0003	Disk Reset --
				ENTRY - none,		EXIT - none
			Simply resets the Host Buffer Active flag and the
			Unallocated Sector Counter.  This follows exactly the
			definition in the latest versions of DRI documentation
			(warm boot). The Kaypro ROM's used this entry point
			for other internal purposes.

0009	Initialize Hardware --
				ENTRY -- DE points to list of port,data pairs
					 A  number of entries in list (len/2)
					(see TURBO-BS.PRN for example of use)
				EXIT  -- none

			This entry allows the physical devices to be set up
			with any byte pattern.  The original Kaypro entry
			point always used its default values.


000C	Home --
				ENTRY -- none,		EXIT -- none

			This entry point follows the DRI definition, of
			reseting the Host Buffer Active flag if the buffer
			does not have a pending write.  It also calls the
			set track entry with an argument of zero.  The
			Kaypro ROM's in many cases also performed a
			physical seek to track zero.  This is unnecessary.

000F	Select Disk --		ENTRY -- C - desired logical drive 0-15
					 E - bit 0=0 if this is first select
							else bit 0=1

				EXIT  -- HL = points to DPH for this drive
						if select was successful
					    = 0000 if either drive does not
						exist or the floppy format was
						not determinable

			The main differences from almost all of the Kaypro
			ROM's is the correct use of the lo order bit of the
			E register as specified by Digital Research.  This
			means that any program that correctly uses the BDOS
			facilities to log in a new drive will have the
			media correctly determined after a disk change.  On
			the Kaypro ROM's the only time a change could be
			made between say single and double sided disks was
			after a warm boot.  Popular programs like SWEEP
			could not be used with a mixture of disk formats.
			(Note that Plu*Perfect Systems' CP/M enhancements
			included a BDOS patch to correct this, when the
			TURBOBIOS is installed this patch is overwritten and
			original contents replaced)

0015	Set Sector --
				ENTRY -- BC = logical sector for next request

				EXIT  -- none

			This routine combines the functions of the old
			Sector Translation routine.  It must be called
			after the select disk function has been called, so
			that the correct sector translation table can be
			used. This is identical to the BDOS use of the
			original two separate entry points.


0021	Sector Translation --
				ENTRY -- BC = logical sector for next request
					 DE = pointer to translation table

				EXIT  -- HL = logical sector

			This routine is a totally dummy routine and for
			efficiency all of its functions are now performed
			in the Set Sector Routine.


0027	Motor Off --
				ENTRY -- none,		EXIT -- none

			Before performing its major deselect function this
			entry check the Host Buffer for a pending write and
			if there is one the buffer will be written to disk.
			This ensures that whenever the select lights are
			off that disk accurately reflects the contents of
			the Host Buffer. It is thus good practice to remove
			floppy diskettes from the drives only when the select
			light(s) are off.

			This entry will then turn off the floppy drive spindle
			motor, and, if the Advent Personality Decoder board
			is not present will deselect the floppies so that
			the select light goes off.  If Hard Disks are
			present then each drive seeks its innermost
			cylinder and then non existant drive 0 is selected
			which will turn off the select lights on the drives.
			
0048	Ten Millesecond Delay --
				ENTRY --   A = multiplier for delay

				EXIT  -- none

			This entry point provides the correct delay
			regardless of processor clock speed.  All Kaypro
			ROM's assume a 4 MHz clock.  In addition, if the
			keyboard type-ahead is enabled then the keyboard is
			continually polled during the delay and any
			keypresses are serviced and placed in the buffer.
			The accuracy of this timer is within 4%, note that
			it reflects the effective CPU speed at cold boot
			and if the speed is changed (as is possible with some
			speed up modifications) the timing will no longer
			be accurate.

(# New Entry Points available in TURBO ROM)

004B	Serial Printer input status --
				ENTRY -- none
				EXIT  --  A = 00 and Z if no character ready
					    = FF and NZ if character ready

			This entry allows use of the extra serial printer port
			on 84 machines.  On 83 ROMs this entry is double
			mapped to the serial data port.

004E	Serial Printer port input --
				ENTRY -- none
				EXIT  -- A = character recieved


0051	Serial Printer port output --
				ENTRY -- C = character to be sent
				EXIT  -- none

0054	Serial Printer output status --
				ENTRY -- none
				EXIT  -- A = 00 and Z if not ready
					   = FF and NZ if ready for next

0054	Reload System  --
				ENTRY -- DE = Address to load system tracks
					 B  = number of sectors to load
					 C  = starting sector to load
					 A  = logical drive to load from

				EXIT -- none,  any errors force cold boot

			This entry point will reload all or part of the
			operating system from the system tracks of the
			specified drive.  The usual conditions of 40
			sectors/track will cause floppy type load and > 55
			sectors/track will cause RAMDISK or Hard disk reload.

005A	Next Screen Dump Character --
				ENTRY -- C = FF if first screen character

				EXIT  -- A = character (masked with 7FH)
					 L = column (00 means new line)
					 Z flag set if end of screen

			This entry allows external programs to read the
			screen whether this is an 84 or 83 machine.  The
			flashing attirbute on the 83 machines is removed and
			on 84 machines all pixel graphics are replaced with
			blanks.  It is the responsibilty of the calling
			program to insert new line characters if needed.

005D	Set Cursor Type ---
				ENTRY --  A= cursor definition

				EXIT  -- none

			This entry is machine dependent.  On 83 mahines the
			definition is simply the character itself (with or
			without the hi bit set for flashing).  On 84
			machines the definition character has the same
			meaning as the "n" used in the ESC U n cursor
			setting sequence.

0060	One Millesecond Delay  --
				ENTRY --  A=delay multiplier
				EXIT  --  none

			See description of Ten Millesecond above.

0063-6A on 83 machines are not to be used.  These are used internally by
the ROM initialization code and will have unpredictable results if called
by external routines.

	--  84 machines only ---
All the entry points below have the same parameter interface
				ENTRY --  none
				EXIT  --  H = BCD hours
					  L = BCD minutes


0067	Kaypro Clock --
			Returns current time from built-in Kaypro clock

006A	Advent Products Clock --
			Returns current time from Advent clock

006D	Kenmore Z- TIME Clock --
			Returns current time from Kenmore clock


NOTE: Clock must exist as no internal checking is done, and unpredictable
results are possible if wrong clock is read.

r itself (with or
			without the hi bit set for flashing).  On 84
			machines the definition character has the same
			meani