*** NOTE ***   12/11/84   DEVICE.DOC

     The  December  issue of BYTE magazine contains an  excellent 
article  by Steve Ciarcia (as usual) on using micros  to  control 
the real world.
                                        --J.F.

*** NOTE ***   11/25/84

     I   just  glanced  through  the  December/January  issue  of 
Profiles  and saw a "home control system" for your Kaypro in  the 
"New Products" column.   While the DEVICE setup described in this 
file  is no where near as complex as the system described in  the 
magazine,  it doesn't carry a $1500.00 price tag either.  I think 
that every computer owner,  at one time or another,  dreams of  a 
"computerized" household. DEVICE is just my way of automating the 
troublesome  task  of  hooking  up  various  printers  and  other 
peripherals  while,  in a rather small fashion,  fulfilling  this 
dream.   If  you  are of the more ambitious sort and  plan  on  a 
similar,  but  more  extensive  system,  I  hope DEVICE can be of 
some  small help to you,  possibly as a starting point.   In  any 
case, good luck and happy computing!     
                                        --J.F.

DEVICE.DOC -- Documentation for DEVICE vers 1.1
              November 21, 1984
              (for use with pre-'84 Kaypro IIs and 4s only)

     The longer that I own a computer,  the more gizmos, gadgets, 
and do-hickeys I accumulate for it.  Of course, every time I want 
to  use one of these assorted goodies,  I have to swap a  zillion 
cables and extension cords.  

     I looked at various RS-232 switchers, etc,  but none of them
seemed to satisfy my (or my wallet's) requirements.  Some digging 
around (my favorite pastime!) showed that my Kaypro 4 had two Z80 
PIOs,   but   only used one side of each.   I decided that one of 
these would satisfy my "switching" needs nicely.

HARDWARE
--------
     I selected the unused B side of the general purpose PIO (the 
A  side  is used for the Centronics printer port) as  my  victim.  
Bits 0-7 of this spare parallel port are available at solder pads 
E7-E14 on the main board (next to U54) of older (pre-'84) Kaypros 
(see  the  table below),  and can be brought to the back of  your 
Kaypro,  along with +5 volts D.C.  and supply ground,  using some 
ribbon cable and a small "D" type connector.
 
          bit #  - solder pad
          -----    ----------
            0         E14
            1         E13
            2         E12 
            3         E11
            4         E10
            5         E9
            6         E8
            7         E7

     Each  of  these eight lines can be used to  control  various 
peripherals,  etc.  in a variety of ways.  The following circuit, 
for  example,  allows  your Kaypro to control the  flow  of  A.C. 
current to a given load.
                                                  
          inverter        +5              ----------+------->120
                           |    ______    |         |M2   __>VAC
             |\            ---1| MOC  |6---         |     |  
             | \    200 ohm    | 3010 |           TRIAC   |
cntrl line---|  >O--/\/\/\----2|      |   r2*   G / |     |
             | /               |      |4--/\/\/\-/  |M1   |
             |/                 ------              |     |
                  * - value depends on triac's      -LOAD--
                      gate current

     The  inverter  allows the PIO to drive the  LED  inside  the 
opto-coupler,  which, by the way, provides a very comforting 7500 
volts  of isolation between your computer and the 120 volts A.C..  
You could substitute a relay for the triac or use the circuit  to 
control  a  lower A.C.  voltage (for low voltage  lamps,  motors, 
etc.).

     The  following  two examples show how to control  either  an 
analog or digital signal buss.

                           ----- 
      8 digital lines in->|     |>-8 digital lines out (buffered)
                          |     |                                
                        e2|     |
             |\       ----|     |
             | \      | e1|     |  74LS244      
cntrl line---|  >O----+---|     |               Digital "Switch"
             | /           ----- 
             |/ inverter

                           ----------
          4 lines analog  |          |  4 lines analog 
          data in-------->|          |>-data out
                          |          |
                 |\        ----------  4066
                 | \      A| B| C| D|           Analog "Switch"
    cntrl line---|  >------+--+--+--+
                 | /
                 |/ buffer

     By using variations of the above techniques,  I have set  up 
my  work  station  so  that I can manipulate  or  enable  various 
peripherals,  including my  printers,  an  EPROM  programmer,   a 
modem, and a speech synthesizer without leaving the keyboard.  

SOFTWARE
--------
     Using  the  spare parallel port is quite  straight  forward.  
The data address is 0AH.  The control address is 0BH.  If you are 
not  familiar  with programming the Z80 PIO I would suggest  that 
you  pick  up a copy of the Mostek data book,  it seems to  be  a 
little easier to decipher than the one available from Zilog.  The 
following   partial   Z80  listing  sets  up  the  PIO   in   the 
bidirectional mode and then sets up all 8 bits as outputs. 

PORT    EQU     0AH    ;SPARE parallel port
CPORT   EQU     0BH    ;PIO control port
CWORD   EQU     0CFH   ;control word to set spare port to 
;                       bidirectional mode.  the PIO expects 
;                       another word after this one to set the 
;                       individual bits to either INPUT or OUTPUT
;                              0 in bit pos. = OUTPUT
;                              1 in bit pos. = INPUT
;    initialization 
        LD      A,CWORD     ;cntrl word in A
        OUT     (CPORT),A   ;output to cntrl port
        LD      A,00H       ;ALL outputs
        OUT     (CPORT),A
;
;    output info to port
        LD      A,byte 1        ;first byte to output
        OUT     (PORT),A        
        LD      A,byte 2        ;second byte to output
        OUT     (PORT),A
         .        .  
         .        .
         .        .
          and so on

     DEVICE.COM is a simple  menu driven program  that allows you 
to  toggle  "devices" 1 thru 8 ON or  OFF (bits 0 thru 7  of  the 
spare  port  HI  or  LOW)  from  the  keyboard.    Simply  enter:    
DEVICE<cr>  to enter the program and either ^C or <ESC> to  exit.  

     Any  settings  that  you make using DEVICE  will  remain  in 
effect until you either change them with DEVICE,  press the reset 
button (Cold Boot), or turn your computer OFF.

     You can strike any key to cancel the pause after the sign-on 
message  (striking  any key also cancels the pause  after  DEVICE 
informs  you of an improper  entry).   You can also remove either 
the sign-on message or the improper entry message (or both)  with 
the patches listed at the end of this file.

     I  have  been using the same basic setup for close to  eight 
months now,  and have had no problems with it.   For me at least, 
the  convenience provided has been well worth the effort it  took 
to get everything "up and running".   I would enjoy hearing  from 
you  if  you set up a similar system or are using your  micro  in 
some other type of "real world" control.  Just leave me a message 
on the Downey RCPM  (213) 806-2226.

                                   ENJOY!
                                     Joe Fitzpatrick
   
DEVICE.COM PATCHES
---------- -------
  Remove sign-on message:  

                   change  0169 from 11H to 18H
                           016A from CAH to 07H

  Remove improper entry message:
                   
                   change  020E from 11H to 18H
                           020F from 07H to 0EH

     If  you  simply want to change the pause length (default  is 
approximately  2 seconds on a 5 Mhz Kaypro) change the hex  value 
at 027A (currently 07H) to a lower value to shorten the pause, or 
a higher value to lengthen it.

Note about DEVICE on PRO8 systems:

     If you are using the PRO8 monitor ROM from Micro  Cornucopia 
(a great magazine!),  DEVICE changes  your cursor  to   invisible 
(SPACE) until you exit the program,  at which time your cursor is 
restored.   This  operation should have no nasty side effects  on 
non-PRO8  systems.  If  one  should  turn  up  however,  you  may 
remove this feature by changing the ten bytes from  015F  to 0168 
to 00H and the seven bytes from 023B to 0241 to 00H.6.