VT100 is a revision of a program that uses the Kaypro to
   emulate some of the functions of a DEC VT100 terminal.  It
   works about the same as the Kaypro-supplied TERM program,
   but intercepts incoming and outgoing codes and translates
   them from/to the equivalent DEC VT100 codes.  The program
   does not buffer I/O, and has a baud rate limitation of about
   2400 (determined empirically).  No attempt has been made to
   optimize the code for speed.  There was a block of
   documentation at the top of the original assembler source
   file, which has been reproduced below.  Some of the codes
   that are translated are explained on the screen that is
   displayed when the program is started.  For the first time
   user, it is worth just running the program "off line" once
   in order to read this first screen.  The program is set to
   run at 1200 baud, no parity, 8 data bits, and 1 stop bit.
   Information on changing the baud rate is in the source
   file.

      The purpose of the revision was to be able to use the EDT
   editor, which makes extensive use of the VT100 keypad and
   the arrow keys.  After a lot of work, only mixed success has
   been achieved.  The program works, but cannot handle the
   screen in the same fashion as a real VT100. Essentially, the
   user must continually repaint the screen to make sure that
   he is editing what he thinks he is.  The problems that still
   remain to be solved involve the scrolling region, and VT100
   set scroll commands which are used in line deletion.  To
   handle this correctly, you would have to keep track of what
   lines are on your screen, and manage them within the
   program.  See a DEC VT100 manual for more information.

      The program expects the keypad and arrow keys to be
   re-configured.  This is done by running the CONFIG program
   that comes on your system disk.  Each of the keypad and
   arrow keys should be set to their original code plus '80'
   HEX, or in other words, the high order bit should be turned
   on.  Once the disk has been re-configured, you must insert
   it in drive A and hit the reset button in back.

      A real VT100 has an extra row of keys above the keypad
   called function keys.  This program emulates these keys by
   using a 'shift' key (the back-slash '\') followed by one of
   the arrow keys, e.g.  PF1 is obtained by hitting the '\' key
   followed by the up arrow key.  If you hit anything except an
   arrow key, the back-slash will be ignored.  To enter a
   back-slash, just hit it twice.

      All VT100 incoming codes should be recognized, but many
   of them are ignored.  See comments in the source listing.
   Unrecognizable codes may produce a debug message, which is a
   colon followed by the byte in hex.  If an escape sequence
   which is unknown to the program appears, the program will
   show a solid block followed by a '[' and the parameters in
   hex.  The assembler source contains code used for debugging,
   it should be edited out before assembly (look for DEBUG with
   an editor).

      The original author was:

       Tony Drake,  13017 Parkland DR., Rockville, MD 20853

      and the current modifier is:

     Jack Mathis, 1363 Birch Hill Rd., Mountainside, NJ 07092

      Comments and/or suggestions are welcome.

      Copyright 1983,1985 by Anthony Drake and Jack Mathis.
   Permission is hereby given to copy and use this material
   freely, as long as no charge is made except for reasonable
   distribution expenses.


      The current assembler source is written for Z80MR, the
   public domain Z80 assembler.

      The following comments were extracted from the top of the
   original assembler code:

   ;
   ;     * WRITTEN FOR MICROSOFT'S MACRO-80 ASSEMBLER
   ;
   ;
   ;     *****************************************************************
   ;     *                                                               *
   ;     *                  DEC VT100 TERMINAL EMULATOR                  *
   ;     *                                                               *
   ;     *  THIS PROGRAM WAS CREATED BY DISASSEMBLING THE KAYPRO "TERM"  *
   ;     *  PROGRAM, THEN EXTENSIVELY MODIFYING IT TO HAVE IT MAKE       *
   ;     *  CODE SUBSTITUTIONS APPROPRIATE FOR A VT100 TERMINAL. NOT     *
   ;     *  EVERY VT100 CODE IS HANDLED (BY FAR). A LIST OF THE CODE     *
   ;     *  FUNCTIONS THAT ARE HANDLED IS DISPLAYED ON THE SCREEN        *
   ;     *  WHEN THE PROGRAM FIRST STARTS UP.                            *
   ;     *                                                               *
   ;     *  NOTE THAT THIS IMPLEMENTATION HAS NO BUFFERING CAPABILITY,   *
   ;     *  AS DOES THE VT100. THIS MEANS THERE IS A LIMIT TO THE        *
   ;     *  AMOUNT OF TIME AVAILABLE FOR CODE PROCESSING WITHOUT         *
   ;     *  LOSING CHARACTERS BEING INPUT. WITH THE STANDARD KAYPRO II   *
   ;     *  CLOCK SPEED, SOME INPUT CHARACTERS WERE LOST WHEN 4800       *
   ;     *  BAUD WAS USED. THIS OCURRED WHEN A CURSOR-POSITIONING        *
   ;     *  SEQUENCE WAS BEING TRANSLATED (THE WORST CASE). THERE IS     *
   ;     *  AN ADDITIONAL CONSTRAINT AFTER THE SCREEN FILLS UP, AND      *
   ;     *  A SCROLL UP IS REQUIRED. THE KAYPRO BIOS PERFORMS THIS       *
   ;     *  IN SOFTWARE, MOVING ALL 1920 CHARACTERS UP. THIS TAKES A     *
   ;     *  NOTICEABLE AMOUNT OF TIME, AND ANY CHARACTERS COMING IN      *
   ;     *  THE SERIAL PORT JUST THEN WILL BE LOST. SO FAR, EVERY-       *
   ;     *  THING SEEMS TO KEEP UP AT 2400 BAUD. THE BAUD RATE IS        *
   ;     *  SET INTERNALLY SO THAT THE "BAUD" PROGRAM NEED NOT BE        *
   ;     *  RUN BEFORE EVERY EXECUTION OF THIS PROGRAM,. THE VALUE       *
   ;     *  USED TO SET THE BAUD IS STORED AT ADDRESS 103H SO THAT IT    *
   ;     *  CAN BE CHANGED WITH A "DDT" PATCH WITHOUT REASSEMBLING.      *
   ;     *  (A VALUE OF 5 WILL YIELD 300 BAUD, 7 GIVES 1200, AND 10      *
   ;     *  GIVES 2400 BAUD. OTHER VALUES ARE POSSIBLE.) THIS VERSION    *
   ;     *  IS SET FOR 1200 BAUD, NO PARITY, 8 DATA BITS, AND 1 STOP     *
   ;     *  BIT. EXCEPT FOR THE BAUD RATE, THESE VALUES ARE DEFINED      *
   ;     *  BY CONSTANTS AT THE VERY END OF THE PROGRAM.                 *
   ;     *                                                               *
   ;     *  COMMENTS/SUGESTIONS: TONY DRAKE (301)-942-0342      NOV '83  *
   ;     *                       13017 PARKLAND DRIVE                    *
   ;     *                       ROCKVILLE, MARYLAND  20853              *
   ;     *                                                               *
   ;     * COPYRIGHT 1983 BY ANTHONY DRAKE. PERMISSION IS HEREBY GIVEN   *
   ;     * TO FREELY COPY AND USE THIS MATERIAL, AS LONG AS NO CHARGE    *
   ;     * IS MADE, EXCEPT FOR REASONABLE DISTRIBUTION EXPENSES.         *
   ;     *                                                               *
   ;     *****************************************************************
   ;