BIOSMR12
                            ========



The accompanying files represent a modification to the  excellent 
job  Michael  Rubenstein did with his BIOSMMR.   I wanted to  add 
some  features  to  speed up the cold boot  process  as  well  as 
incorporate  ZRDOS+ from Echelon,  Inc.  in place of CP/M's BDOS.  
Since  the  internal structure of the latter is  quite  different 
from BDOS, there were some changes required.  the following notes 
discuss those changes.

For the record,  these files are working with a Kaypro 10 with an 
original issue ROM version 1.9E.   I am using a SWP  Co-processor 
that can be configured as a RAM disk with 1 MB capacity.  


Background
----------

For  those  that  are unaware of it,  BIOSMMR  is  a  significant 
improvement to the Kaypro BIOS by the above mentioned author.  It 
supports  a  number  of outstanding  features.  Full  redirection 
allows   saving  console  output  to  a  disk  file  printer   or 
combination of both.   Fast boot and fast reset greatly speed  up 
operation  at the system level.   (try hitting Control-C on  your 
standard  BIOS  - takes  about 5-6 seconds to  come  back.   With 
BIOSMMR  and FASTBOOT,  comes back in under a second!)  The  hard 
disk  capacity  is increased from the standard 4472K per side  to 
5016K  per side.   There are other features,  but these  are  the 
highlights.   The  initial distribution consisted of over 250K of 
source code,  utilities and documentation.  The reader is assumed 
to have those files in order to fully understand the following as 
well  as  having the utilities to access the  enhanced  features.  
After operating with this BIOS for over 6 months,  I would  never 
go  back to a standard "slow" BIOS.   It truly make the Kaypro 10 
"fly".  However, never one to leave well enough alone, there were 
two changes I wanted to make.


Faster Coldboot
---------------

When  a  Kaypro  10 coldboots,  it  loads  the  graphics  overlay 
routines  from the B drive as placed on the B drive system tracks 
by PUTOVLxx.   Then, it links to the system tracks of the A drive 
to  load CCP,  BDOS and BIOS.   Since ZCPR3 requires  SYS.ENV  be 
loaded  before running any utilities,  including a STARTUP alias, 
BIOSMMR had the following command line hard-coded into the BIOS:

                      LDR SYSxx.ENV;STARTxx

In  addition  to taking up a little extra  BIOS  space,  it  also 
slowed  the  cold boot process since STARTxx had to load ALL  the 
system segments.   Using the procedures outlined below, the PATH, 
named  directory  and SYSxx.ENV are all auto-loaded  from  the  B 
drive.   This feature is enabled by setting the equate "fload" to 
-1 in BIOS.LIB.


ZRDOS+ BDOS Replacement
-----------------------

After  recently  acquiring ZRDOS+,  I find the features are  very 
nice,  the speed is slightly improved and the ZRDOS+  accessories 
are handy and fast.   Unfortunately, BIOSMMR hot-patches BDOS for 
fast  reset  and  redirection.   New equates in  BIOSLOC.LIB  are 
conditionally  selected  by setrting the equate "zsys" to  -1  in 
BIOS.LIB.


Installation
------------

The  following  alias scripts are used to assemble and  load  the 
various elements of the ZCPR3 system.   To get started the  first 
time,  I  suggest  uou manually type in the appropriate  assembly 
commands.

1.  LOADZCPR  - assemble  and load the  ZCPR3  command  processor 
replacement into the PUTSYS file:

IF EX $1.ASM
MAC $1 $$PZSZ
SAK /BP3 CTRL-C TO ABORT
MOVHEX 980 $1
MLOAD $2.COM,$1
ERA $1.BAK
ELSE
ECHO LOADZCPR <ZCPR3.ASM FN> <PUTSYS.COM FN>
FI

2.  LOADBIOS  - assemble  and load the new BIOS into  the  PUTSYS 
file.   This  script also runs the resultant PUTSYS and  re-boots 
the machine.   This can be avoided by typing CTRL-C at the second 
prompt.

IF EX $1.MAC
M80 =$1
SAK /BP3 ^C TO ABORT
RELHEX $1
MLOAD $2.COM,ZEROBIOS,$1
ERA $1.REL
ERA $1.BAK
ERA $1.HEX
SAK /BP5 ^C TO ABORT
$2
COLDBOOT
ELSE
ECHO LOADBIOS <BIOS.MAC FN> <PUTSYS.COM FN>
FI

3. LOADENV - this script assembles and loads the ENV segment into 
the PUTOVL file at the appropriate load point.

IF EX $1.ASM
MAC $1 $$PZSZ
MOVHEX E80 $1.HEX
MLOAD $2.COM,$1
ERA $1.BAK
ERA $1.HEX
ELSE
ECHO LOADENV <SYSENV.ASM FN> <PUTOVL.COM FN>

4.  LOADNDR - this script assembles and loads the named directory 
file,   as  created  by  MKDIR,  into  the  PUTOVL  file  at  the 
appropriate load point.

IF EX $1.NDR
CP $1NDR.COM=$1.NDR
UNLOAD $1NDR
MOVHEX C00 $1NDR
MAC PATH $$PZSZ
MLOAD $2.COM,$1NDR,PATH
ERA $1NDR.HEX
ERA $1NDR.COM
ELSE
ECHO LOADNDR <NAMES.NDR FN> <PUTOVL.COM FN>
FI

5.  LOADXCP - this script is used to assemble and load either the 
FCP  or  RCP segments.   These segments must be loaded by LDR  at 
STARTUP.

IF EX $1$2.ASM
MAC $1$2 $$PZSZ
MLOAD $1$2
REN $1.$2=$1$2.COM
ERA $1$2.BAK
ERA $1$2.HEX
ELSE
ECHO LOADXCP <SYS> <FCP OR RCP>
FI


Files  required  on the same drive and user area to  execute  the 
above assembly are listed below.   Those included in this library 
are indicated by (*); those included in BIOSMMR.LBR are indicated 
by (+).

Source Files
============

ZCPR3.ASM, Z3BASE.LIB(*), Z3HDR.LIB(*)

BIOS.MAC(*), BIOS.LIB(*), BIOSLOC.LIB(*)

SYSENV.ASM, SYSENV.LIB

PATH.ASM(*)    (Sets the default path at cold boot)

NAMES.NDR

SYSRCP.ASM, SYSRCP.LIB

SYSFCP.ASM, SYSFCP.LIB

ZEROBIOS.HEX(*) Loads a zeroes in unused BIOS locations.

BIOS.HEX(*)    My current BIOS with the features indicated
               in the accompanying  BIOS.* files.  This is
               for a 50K system.


Programs and Utilities
======================

Program   Used in
-------   -------

M80            LOADBIOS

MAC            LOADZCPR, LOADENV, LOADNDR, LOADXCP

MLOAD(+)       LOADZCPR, LOADBIOS, LOADENV, LOADNDR, LOADXCP

MOVHEX(+)      LOADZCPR, LOADENV, LOADNDR

RELHEX(+)      LOADBIOS

UNLOAD(*)      LOADNDR (Creates a .HEX file from a .COM file)

COLDBOOT(*)    LOADBIOS (Coldboots the Kaypro 10)

PUTSYSxx       LOADZCPR, LOADBIOS (Your system loader)

PUTOVLxx       LOADENV, LOADNDR (Your overlay loader)


Sample System Aliases
---------------------

1.  START50 - This is my startup alias.   SETCUR and SCRNPRNT are 
from  BIOSMMR.LBR.   SETCUR  gives program control of the  cursor 
style;  SCRNPRNT is a screen dump utility.  My root: directory is 
A15:.

A15:
LDR SYS.RCP,SYS.FCP
SETCUR BLOCK STEADY
SCRNPRNT

2. RAM - This alias sets up my Co-power plus board as a RAM disk.  
The  RAM disk driver is loaded at location EA00,  as provided  by 
BIOSMMR, and defined as drive D.  KSTAT, FASTBOOT and FASTSUB are 
BIOSMMR utilities.   AC is a ZRDOS copy utility.   KSTAT sets the 
maximum allowable disk to D:.  AC copies the appropriate files to 
the ramdisk for faster operation.   The path is redefined to look 
at the ramdisk first.   Then the named directories are  redefined 
to  recognize  the  ramdisk.  Finally FASTBOOT  and  FASTSUB  are 
enabled.
 
RAMDISK D,,EA00
KSTAT DSK=D:
AC D0:=A8:*.* /N
PATH D0: A15: A$:
A0:
LDR RNAMES.NDR
FASTBOOT D:BOOT.SYS
FASTSUB D:
$D$U:


Closing Comments
----------------

I realize these notes are somewhat sketchy.   I would be glad  to 
answer  any specific questions but,  before you ask,  please  get 
BIOSMMR.LBR  and  study the original.   I check in  approximately 
weekly  at  Z-Node Central 415-489-9005  and Pro-Comm  Data  Base 
813-937-3608/813-937-6829. BIOSMMR.LBR is available at the latter 
location.    Note that M80,  MAC and ZRDOS+ are NOT public domain 
programs.


John Smith
Pepperell, MA
September 15, 1985