RSX system Documentation (84/01/25)
               ===================================

What is an RSX  (Resident System Extension for CPM 2.2 only)
==============

An RSX is a method of adding new system calls to the CPM system,  which can
then be called just like any other BDOS function.  The RSX can also be used
to intercept native calls and change their operation (ex. list output calls
could be intercepted and spooled,  or a program can "chain" to an arbitrary
program by passing the command line).  The RSX is also a mechanism (in this
implementation)  for installing new/revised i/o drivers,  such  as  foreign
disk systems,  keyboard translators,  spoolers,  etc.   This was written to
implement the "chain" ability.


Executing an RSX
================

Under this system,  an RSX is stored as any other .COM file.  To install it
the .COM file is executed by typeing its name at the CCP prompt.  To remove
it enter its name again.   In between installation and removal the RSX will
be memory resident,  and warm boots will not reload the CCP or BDOS system.
At the same time the added BDOS call(s) or drivers are available.

CAUTION:  Some  systems  require a physical reboot (eg Kaypro 4) to  change
disk formats (density, single/double sided, etc).  This will not occur when
the RSX is active.

CAUTION:  The original Digital Research CCP will not start up a SUBMIT  job
when  the RSX is active.  In addition logging on to an invalid  drive  will
hang  the system until a reset.   You can avoid this by installing  CCPLUS,
which will also provide automatic drive searches for applications. ZCPR has
not been tested with this system.

Memory usage:
============

The  RSX  is  mounted below the CCP area,  and thus reduces  the  available
application  memory.    The  utility  HOWBIG  shows  the  effective  memory
available at any time.  Just enter d>howbig


Making a new RSX  (This system is for CPM 2.2)
================

Obviously,  someone must write the system code needed.   That is you.  This
system provides a standard method of installing and removing the code  from
your  running system.   The file RSX.Z80 is heavily annotated to show where
the custom code should be inserted.  The RSX installed by this only outputs
a  short message when called by an application program.   You can  test  by
loading  it,  then  under  DDT create system calls with  the  argument  100
(064h).   If  the  (de)  argument is 0 the returned value is 0 for  no  RSX
present,  non-zero  if  present  and active.  If the (de)  argument  is  -1
(0ffffh)  the RSX is made inactive,  and will be removed on the  next  warm
boot (^C).  Alternatively the utility ENQUIRE can be used to pass arguments
and display the results.  Usage (parameters in hex) is:

d>ENQUIRE rsxnum [param]     which executes BDOS call rsxnum, with de=param

To create a new RSX, you must first assemble (or relocate) two versions

    rsxzero.$$$    is "orged" or relocated to start at 0
    rsxone.$$$     is "orged" or relocated to start at 0100h (normal)

With DDT, load RELOCCP.SYS, and append, at 0200h, rsxzero.$$$ by

    B>DDT reloccp.sys
    ...signon etc...
    -irsxzero.$$$
    -r100                  (note the 0100h offset command)
    .....info. returned    (This assumes a .COM type file.  If it is)
                           (a hex file with .HEX extension use r200)

Now examine the bytes loaded at locations 203 thru 204

    -d200,204
    0200 C3 00 54 30 05    <--note this number, hex 0530, right byte 1st
                              (number is for example only)

Now find the location (-0100h) of the first free byte in the relocated
image by:

    -h100,530
    0630 0430              <--The left number (0630) is what you want

and append the 0100h based image by

    -irsxone.$$$
    -r630                  (using the above number as offset)
    Next  PC  Save
    nnnn 0100    m         (The "save" value from DDTY only)

Note  the "next" value loaded,  use the left two digits as a hex number and
save that number of pages.  (DDTY5 will tell you in decimal) by exiting and
executing save

    -^C                    (control-c)
    A>SAVE 12 temp.com     (The "12" is for example only)

Now execute temp.com.  It will tell you how much to save

    A>temp
    now SAVE 7
    A>SAVE 7 rsx.com                    (do it)

You now have a usable new version of RSX,  which will relocate itself  into
high memory when executed.

If  you are using other systems mounted below CCP in high memory,  such  as
KEYS  or  one  or more additional RSXs,  the first such  loaded  will  have
protected  the  CCP memory (of 2k),  and a further run of RSX will  save  a
totally  useless additional 2k.   To avoid this by having the loader detect
this situation and automatically avoid the extra memory save do:

    A>ddt rsx.com
    ....signon etc...
    -ireloccp.ovr                  (the "smarter" overlay for load only)
    -r
    -^C                            (control-c)
    A>save 7 rsx.com               (same number as before)

and you are all done.


RSX call conventions
====================

When the RSX is installed it appears as a new CPM BDOS call,  identified by
the  value in C,  and receiving a parameter in DE.   The DE parameter  will
usually   be   a   pointer to some user memory  area,  e.g.  an  FCB.   The
following parameter values have been reserved (Note that under CPM a  valid
pointer to usable memory can never have these values):
     0    Residence  enquiry.   If  the RSX is mounted and active  it  will
          returng  a non-zero value in A.   If not mounted or inactive zero
          is returned (as will BDOS 2.2 for any invalid calls)
     1    Return  a pointer (in HL) to any data areas specific to the  RSX.
          ex:   disk   drive   parameters  for  a  general   foreign   disk
          reader/writer,  or table of key translation strings for a console
          key redefinition system.   If the RSX is not resident or does not
          use such an area obviously the pointer is invalid.  The code that
          uses  such a pointer is specific to the RSX,  and thus this usage
          is optional.
    -1    (or 0FFFFh).  Remove the RSX.  The memory used will be reclaimed,
          if possible, on the next warm boot.

A limitation
============

Only one RSX (the first installed) can provide i/o drivers visible to BDOS.
Any  further  ones cannot reliably find/modify/restore the  BIOS  pointers.
Thus checks have been built in,  and the user equate "driver", or patchable
variable "chkflg" cause these checks to be executed.   However,  later RSXs
can  install bios modifications visible ONLY to application programs  using
direct BIOS calls through the pointer at location 1.  KEYS is an example of
an  RSX providing BDOS visible bios changes (although  built  earlier,  and
does not use this exact mechanism).

                                   C.B Falconer  (85/Jan/25)