PCINPUT.BAS
                                 PCGOTO.BAS
                                 PCCOPY.BAS

                                 Ernie Graves
                                 June 1, 1984


             Do you ever need to copy large amounts of data from one
        PerfectCalc spreadsheet to another without linking the two
        spreadsheets or from a data base file to a PerfectCalc spread-
        sheet?  This disk contains three Microsoft Basic programs to
        accomplish these tasks without tedious manual entry of data on
        the new spreadsheet.

             The files on the disk include:

        PCINPUT.BAS      PCINPUT.COM      PCINPUT.DOC      V100FILE.PC
        PCGOTO.BAS       PCGOTO.COM       PCGOTO.DOC       V100FILE.DTA  
        PCCOPY.BAS       PCCOPY.COM       NS.COM           V100FILE.DOC
                                                           V100PART.DOC
                                                           V112FILE.PC

             The three MBASIC programs are described below, and more
        explanation is included in the programs themselves.  NS.COM
        and the data files are included to permit viewing the various
        types of data files so as to grasp more quickly just what the
        programs are doing.  The data files are also convenient for
        experimentation and practice with the programs.

             Numbers that do not depend upon formulas can be copied from
        one PerfectCalc spreadsheet to another using the "two-windows"
        procedure of PerfectCalc's multiple file handling capability.
        So can labels.  However, if a number depends upon a formula,
        the two spreadsheets must be linked by a reference entry, and
        both spreadsheets must have been loaded into memory for the new
        spreadsheet to display the "copied" number without an "Error!"
        message.  Such a number isn't really copied, only referenced.

             Each of the three MBASIC programs on this disk overcomes
        this problem by processing the contents of a disk file to create
        a new PerfectCalc spreadsheet file that is able to display all
        the numbers free of formulas.  This is useful when you have
        finished using the old spreadsheet and want to begin a fresh
        spreadsheet using the results of the earlier spreadsheet as a
        starting point.

             The processing can start at any one of four different
        types of data file, each of which stores the entries in a
        different way.  The sample files of the four types are:

        V100FILE.PC     PerfectCalc spreadsheet file, Versions 1.00-1.10
        V112FILE.PC     PerfectCalc spreadsheet file, Version 1.12
        V100FILE.DTA    DataStar comma-delimited data base file
        V100FILE.DOC    Document file with data in a rectangular matrix

             PCINPUT.BAS has the widest application.  It takes data from
        either (1) a comma-delimited data base file or (2) a document
        file with data in a matrix and writes the entries in a separate
        PerfectCalc spreadsheet file on a disk.  If you wish to copy
        numbers that depend upon formulas from a spreadsheet file
        produced with Versions 1.00-1.10, the first step is to use
        the PerfectCalc PRINT REGION command (CTRL-X, p) to write the
        numbers to a separate document file on a disk.  Then use PCINPUT
        to convert the document file to a spreadsheet file.  PCINPUT.COM
        is a compiled version of PCINPUT.BAS that runs without MBASIC.COM.

             PCGOTO.BAS provides another way to copy numbers that
        depend upon formulas from one spreadsheet to another.  To use
        this program requires three steps:

             (1)  On the old spreadsheet set up a column 19 characters
        wide that displays the numbers to be copied in scientific
        notation.  The entries in Column f of the sample spreadsheet
        files show how to do this.  All the numbers to be copied should
        be listed in one column without any intervening blank lines.
        Numbers to appear in the same column on the new spreadsheet
        should be grouped together.

             (2)  Use the PerfectCalc PRINT REGION command (CTRL-X, p) to
        write this column of numbers to a separate document file on a disk.
        V100PART.DOC is a sample document file containing the numbers from
        Column f of the spreadsheet.

             (3)  Use PCGOTO.BAS to convert the document file into a
        a PerfectCalc spreadsheet file.

             PCGOTO.BAS and the second option of PCINPUT.BAS rely on the
        same concept: create an intermediate document file, then create
        a new PerfectCalc spreadsheet file in order to replace the formu-
        las in the original spreadsheet file with the numbers in the final
        spreadsheet file.  This approach is necessary for spreadsheets
        produced with PerfectCalc Versions 1.00, 1.02, 1.05 and 1.10.
        The data files produced by these versions do not include the
        numbers which result from the formulas, only the formulas them-
        selves.

             PCCOPY.BAS processes the old spreadsheet file directly.
        It works only with files produced with PerfectCalc Version 1.12.
        It copies either the entire spreadsheet or a rectangular region
        of the spreadsheet selected by the user.  The position of the
        entries on the new spreadsheet is the same as on the old spread-
        sheet.  Data files produced by Version 1.12 include both the
        formulas and the resulting numbers, paired in the same entries.
        PCCOPY.BAS removes the formulas so that the numbers no longer
        depend on them.

             PCCOPY.BAS can also be used to process a spreadsheet
        file produced with Version 1.12 so that the formulas can be
        read by earlier versions, such as 1.00, 1.02, 1.05 and 1.10.
        Without such processing the earlier versions cannot solve the
        formulas in a spreadsheet produced by Version 1.12.

             Each program includes instructions on entering file names
        and spreadsheet parameters.  For the programs to run properly
        it is essential to enter the spreadsheet parameters accurately
        without any extra spaces.  Each program displays the entries
        that are output to the new spreadsheet file.  In addition you
        can check the contents of the input and output files with the
        CP/M TYPE command or NS.COM.